INSTALLING THE OEM SERIAL NUMBER


Space for a 24 bit user number and an 8 bit OEM serial number
is located in MS-DOS. These values are returned by the GET_VERSION
system call.  To patch this value, load msdos.sys under debug, and
search for the sequence of hex values 00 00 00 FF 02 0B.  The
three nul values should be patched to reflect the user number,
and the FF value should be set to the one byte OEM number.
These values will be found at approximately offset 0C40 from
the beginning of MSDOS.SYS

    DEBUG MSDOS.SYS <ret>
    -S 100 FFFF  00 00 00 FF 02 0B <ret>
    0BA0:0C40
    -E 0C40 <ret>
       00 xx <space> 00 yy <space> 00 zz <space> FF nn <ret>
    -W <ret>
    writing xxxx bytes
    -Q <ret>

In the above example, xx yy zz are the user number and nn is
the official OEM number.

OEMs should request an OEM number from Microsoft if they
want one of their very own, this prevents selecting one someone
else already has.