Function Keys and IBM Compatibility
     
	Several OEM's have inquired about making the function keys work
	exactly as they do on an IBM PC.  This is accomplished in the 
	following manner:
	
	Edit STDSW.ASM to set MSVER  EQU FALSE and IBM EQU TRUE.  Now 
 	reassemble DOSMES.ASM which contains the edit function assignments. 
 	This will assign the function keys in the same manner as IBM has done.
 	
	However, the "CANCEL" key in STDSW.ASM which is set to CONTROL X for
 	the generic version of MS-DOS and to the ESCAPE key in IBM DOS, is
 	still not affected by reassembling DOSMES because this assignment is
 	made when STDIO.ASM is assembled.  Therefore, if you are a source
	licensee, reassemble STDIO.ASM as well and all your function keys will
 	then work as on the IBM PC.
	
	If you are not a source licensee, STDIO.OBJ may be patched using
 	DEBUG.  Be sure you have a backup copy of your diskette before you
 	start, as it is easy to destroy diskettes by mistake with absolute
	disk writes.  The DEBUG dialog should look like this:
	
	     debug stdio.obj
	     -u 0403
	     08F7:0403 3C18		CMP	AL,18
	     -e 0403
	     08F7:0403	3C. (hit the space bar)    18. (type 1B <cr>)
	     -w
	     Writing xxxx bytes
	     -q
	
	     debug stdio.obj
	     -u 0403
	     08F7:0403	3C1B		CMP	AL,1B
	     -q
	
	The above dialog changes the "CANCEL" edit character from 18h which is
 	control X to 1Bh which is ESC.