HDDMA.DOC                Version 1.2

The following is a list of diagnostic tests to be used with
the HDC/DMA and a seagate M5. There are different routines for
different test systems (i.e. one drive,two drives,etc.).
Up to four M5's can be tested on one system.
To determine what a routine will actually do, the file can be viewed
simply by using the built-in CP/M command "TYPE".
    (i.e. TYPE<space><filename> <CR>)

Choose one of the following routines for the desired test system:

HDDMA   <For testing two M5's, one selected as "E" and "G";
         the other selected as "F" and "H".  Contains WRLOOP.
         Generally the test used by the technician.>
HDDMA/  <For use with one M5 selectable as "E", "F", "G", or "H".>
                 <Used for final Q/C>
HDDMA%  <For use with four M5's, one as "E", one as "F", etc.>
HDDMA+  <The same as HDDMA except uses a longer, more in-depth test.
         Only Ports #2 and #3 (drive E and F) are used.>
HDDMA@  <Same as HDDMA+ except only Ports #4 and #5 are used.>
HT7.COM <See HT7.DOC>
HT7-1   <Automatically chooses the correct options in HT7.COM for
         testing with one M5.>
HT7-2   <Same as HT7-1 except for two M5's.>
HT7-4   <Same as HT7-1 except for four M5's.>
FMT0    <Formats track 0, drive 0 only. Used for repairing track 0
         after testing an HDDMA board that has written to the M5 during
         powering up or down.>
FMT4    <Runs a quick format test on all four data ports.>
M5TST   <Loads drive 0 with the appropriate files and operating
         system in order to run an overnight pip test.>
M5TST&  <Same as M5TST except more thorough. Every sector of the M5
         is written to and read back. Generally used for thermal HDDMA's.>
M5TST-  <Same as M5TST except shorter. Only the files needed are used.>
M5FNL.SUB  <Used to "bring down" drive E from overnight testing.
            CAUTION: After aborting the "SUBMIT POSTBURN" test,
            be sure to type: DDT <CR>
            From the "-" prompt, type: GF800 <CR>
            The reason for this is that the file "M5FNL.SUB" erases
            all files on drive "E".  The "SUBMIT POSTBURN" test is
            set up to run with the M5 as drive "A", the floppy then
            becoming drive "E". To get the M5 to come up as "E", DDT is used
            to reboot CP/M from the 8" floppy. By forgetting to use DDT
            the floppy disk is still drive "E" and the file "M5FNL.SUB"
            procedes to erase what is supposed to be the M5, but in
            fact is the floppy disk. This results in having to go in
            with "DU.COM" and recover all the files. For a clearer
            understanding, type: TYPE M5FNL.SUB <CR> to view the contents.>
               (See FIX.DOC)

MOV62   <Constructs 62k CP/M and loads it onto drive 0 or "E".>
PIPTST  <Used for troubleshooting HDDMA boards with verify errors,
         disk write errors,cannot close destination file errors,etc.
         Pips to drive 3, or "H".>
WRLOOP  <For checking write gate levels on the HDDMA.>

    To execute a routine, type: SUB<space><filename>  <CR>

                          3/17/83  tm