hdrdwr: writes aa's to first 8 bytes of upper ram, reads back
	and compares.  Checks for error conditions.  Does con-
	tinuous writes of aa pattern to header area, checking 
	for error conditions.  On keyboard interrupt, reads hdrs
	and compares.  When any errors are encountered the pro-
	gram describes the problem on the screen and continuously
	repeats the condition causing the problem.

wrloop: Does continuous writes of aa pattern to header area, even
	without OPDONE.  No messages or interrupts.  Ditto rdloop.

rdsecs: Run under DDT with breakpoint at 147, then dump 150 et seq.
	Rds all headers from Index mark and stores them at 150 et seq
	with first byte of each 5 byte group representing AUX STAT.
	FA in this byte represents CRC error.  F8 means no error.

wrbuff: Continuous writes of 8 bytes of aa patter to beginning of
	upper ram.  No messages.  Ditto rdbuff.  Does not read or
	write from Disc.

hdtest: Allows selection of head and pattern to write, or just reads,
	in loop with no msgs.  Results in clean scope pattern of
	header reads or writes.

steptst: Steps back and forth from tk00 to tk200 to check stepping.