* Documentation FOR DU (DISK UTILITY) AND DDU.

* 		----DU.ASM----

* OVERVIEW:
* 	Originally written to reconstruct erased directories,
* or directories where info was overlaid.  Thus allows dumping,
* by group, track, sector, filename, etc. and patching.  Allows
* ascii or hex scan of the disk.  Maps the location of files
* on the disk by group.  You should know the format of a CP/M
* disk if you're going to diddle with DU.

* USAGE:
* 	DU.ASM provides an overview of the file.  DU has a
* built in help function ? which tells the format of all
* commands.

* DEPENDENCIES:
* 	"Standard CP/M 8" disks" - i.e. 77 tracks,
* directory at track 2.  Standard CP/M scramble factor
* (but could be changed in the .ASM file) etc.  It also works
* on such disks as Northstar CP/M 1.4 which the excellent
* Lifeboat BIOS make "look" like full sized disks in terms of
* sector/track etc.

* FUNCTIONS SUPPORTED -

*	TNN	SEEK TO TRACK NN (NO READ)
*	SNN	POSITION TO SECTOR NN, AND READ
*	GNN	POSITION TO GROUP NN AND READ.
*	G	SHOWS CURRENT POSITION
*	V	VIEWS THE CURRENT SECTOR.
*		(ASSUMES ASCII DATA)
*	VNN	VIEWS NN SECTORS
*	FNAME	PRINT DIRECTORY FOR FILE "NAME",
*		THEN POSITIONS TO IT'S DIRECTORY 
*		SECTOR.

*	=STRING	ASCII SEARCH, STARTING AT CURRENT
*		SECTOR.  <XX> HEX MAY BE IMBEDDED,
*		OR USED ALONE:  TO FIND "IN 0FEH":
*		=<DB><FE>

*	L	RE-LOGS IN THE CURRENT DISK. YOU MAY PULL
*		OUT A DISK, PUT IN A NEW, AND "L" JUST
*		TO LOG IT IN (PREVENTS 	CP/M 1.4
*		FROM GETTING R/O ERRORS). (HMMM, ON SECOND
*		THOUGHT, I'M NOT DOING ANY BDOS CALLS
*		ANYWAY, SO NO R/O ERRORS COULD OCCUR..
*		OWELL, BETTER SAFE THAN SORRY)

*	LX	LOGS IN DISK 'X', SUCH AS: LB

*	D	DUMP SECTOR, HEX + ASCII
*	A	DUMP SECTOR, ASCII ONLY
*	H	DUMP SECTOR, HEX ONLY
*
*	D0,7F  IS THE SAME AS JUST D
*	D3,5
*	A20,3F

*	CHADDR,VAL,VAL,VAL... CHANGE HEX IN SECTOR
*	CAADDR,CHAR STRING... CHANGE ASCII IN SECTOR
*		NOTE THAT <XX> MAY BE HEX IMBEDDED
*		IN THE ASCII:  CA0,OK<D><A><1A>

*		----> USE W TO WRITE CHANGES TO DISK.
*		NOTE THAT THE C COMMAND ECHOES
*		THE OVERLAID DATA FOR VERIFICATION.

*	CHADDR-ADDR,BYTE
* OR	CAADDR-ADDR,BYTE	REPEATS A CHANGE

*	+	ADVANCE 1 SECTOR (IF BELOW TRACK 2,
*		THIS ADVANCES TO NEXT NUMERICAL, IF
*		2 OR >, ADVANCES BASED ON CP/M'S NORMAL
*		SECTOR SCRAMBLING ALGORITHM, I.E. SO +
*		WILL GET THE NEXT LOGICAL SECTOR OF THE FILE

*	-	BACKS UP 1 LOGICAL SECTOR

*		NOTE + AND - MAY TAKE AN AMOUNT:
*		FOR EXAMPLE, +F STEPS IN 15 SECTORS

*	?	GIVES COMMAND SUMMARY
*
*	M	DUMPS A MAP OF THE GROUP ALLOCATIONS
*		FOR FILES.
*	MN	SHOWS WHICH FILE IS ALLOCATED TO
*		GROUP "N".

*	R	READS THE SECTOR CURRENTLY POSITIONED TO
*		INTO MEMORY.  NOTE R (READ) IS IMPLICIT IN
*		THE G, +, AND - COMMANDS, BUT N-O-T IN THE
*		S AND T COMMANDS (I DID IT BECAUSE I WAS
*		TIRED OF DISK READING AFTER T COMMAND BEFORE
*		I HAD A CHANCE TO ISSUE THE S COMMAND)

*	W	WRITE BACK THE CURRENT SECTOR (N-O-T-E MAY
*		NOT BE USED AFTER AN F COMMAND, AS CP/M WAS
*		USED TO FIND THE FILE IN THE DIRECTORY

*	X	EXIT BACK TO CP/M (MUST PRESS RETURN).

*	P	TOGGLE PRINTER SWITCH ON/OFF

*	Z	SLEEP - CAUSES THE PROGRAM TO PAUSE, SUCH
*		AS TO LOOK AT A DUMP.  Z IS 1/10 SEC.  ZNN
*		IS NN TENTHS OF A SECOND ON A 2 MHZ 8080.

*	<	SAVES CURRENT SECTOR IN A SAVE BUFFER

*	>	GETS SAVED BUFFER.  < AND > MAY BE USED
*		TO MOVE A SECTOR TO ANOTHER PLACE.

*	/	REPEATS ENTIRE COMMAND.  DEFAULTS
* OR	/NN	TO "FOREVER".  NN MAY BE 2 TO 0FFH

*		MULTIPLE COMMANDS ARE SEPARATED BY ";"

*	EOT