CONFIG.BAS version 4.6
        Copyright 1987 by George Borys, all rights reserved.

CONFIG.BAS is a patching utility for manipulating the MD2/MD3 system 
image.  All  disk  drive parameters may  be  individually  adjusted, 
including  the number of drives (1 to 4), number of sides (1 or  2), 
tracks per inch (48 or 96), motor on wait times (0 to 1020 mS), head 
settling  times after seek (0 to 1020 mS), stepping rates (1  to  15 
mS), head unload times (16 to 240 mS) and head load times (2 to  254 
mS).   Quad density drives will of course require a modified  format 
program  (like  QFORMAT.COM)  to take advantage  of  the  784K  quad 
density format.

To create a boot disk for a "special" drive (3.5 inch, quad  density 
5 inch, etc.), proceed as follows:

1.   Temporarily configure your hardware  with the  "special"  drive 
     connected as drive C.
2.   Format the special disk and copy the following programs to it:
     CONFIG.BAS
     MBASIC.COM
     SYSGEN.COM
3.   Add a copy of the system image to the special disk:
        C:                    {press [RETURN] }
        SYSGEN                {press [RETURN] }
        A                     {response to "SOURCE DRIVE" prompt}
        [RETURN]              {response to "PRESS [RETURN]" prompt}
        [RETURN]              {response to "DESTINATION" prompt}
        SAVE 46 SYSTEM.CPM    {and press [RETURN], of course}
4.   Invoke CONFIG.BAS by typing:
        MBASIC CONFIG         {press [RETURN] }
5.   Respond to the "FILESPEC" prompt with "SYSTEM.CPM".
6.   Respond  to  the "PHYSICAL DRIVES" prompt with  the  number  of 
     drives that will appear in the final computer configuration.
7.   For each drive in the ultimate hardware configuration,  respond
     to the drive  characteristics  queries  about  single or double
     sided media, 48 or 96 tracks per inch, motor on wait time, head
     settling time  after seek,  stepping rate,  head load time  and 
     head unload time.
8.  Respond to the "UPDATE" prompt by pressing [RETURN].
9.  Install the updated system image on the special disk by typing:
	SYSGEN CPM64.COM        {press [RETURN] }
        C                       {response to "DESTINATION" prompt}
        [RETURN]                {response to "PRESS [RETURN]" prompt}
10.  Reconfigure your hardware in its ultimate  configuration  with 
the "special" drive connected as drive A.  Boot and run!

If you find CONFIG valuable, please consider making a tax-deductable
contribution to BAMDUA  (Bay Area Micro Decision Users Association),
the users group that inspired it all, at:

         BAMDUA
         P.O. Box 5152
         Berkeley, CA  94705