TOPIC : 8080-Z80 AND Z80-8080 SOURCE CODE TRANSLATE PROGRAMS

DATE  : 07 MAY 1986

FROM  : IRV HOFF W6FFC


		 NOTE:	The library name stands for
			I-to-Z and Z-to-I translators.
			This leaves room for a version
			number.


	  NOTE: v2 strips off any high bits that may have been
		set in the the source code being translated.


	The XIZI.LBR contains two translators.	The first is XIZ.COM for
converting Intel 8080 source code to Zilog Z80 source code and the other
is XZI.COM for converting Zilog Z80 source code into Intel 8080 source
code.

	XIZ.COM is by far the most useful of the two.	Nearly all CP/M
programs were originally written in 8080 code.	Most new computers have
been using the Z80 for some years.  Several new macro assemblers have
become available at moderate cost, such as the Echelon ZAS and the very
fast SLR Z80ASM assembler.  Z80MR is a public domain assembler.  Likely
the most common of all is the Microsoft M80 assembler which can handle
either Zilog Z80 source code or Intel 8080 source code (or any mixture
of both with proper instructions).

	If using a Z80 processor, you can use a good translator such as
XIZ.COM to change the 8080 source code into Zilog Z80 source code.  Then
only one assembler will be needed for all your work.  This saves disk
space, procurement costs and notes on how to use the various assemblers
you might otherwise acquire.  (At last count I had 5 for Z80 code and 6
for 8080 code.	It does get a bit silly.)


USING XIZ
===========
	Several options are available, which can easily be set using DDT
or SID:

	0103h	00  defaults to .Z80 extent for the new file
		FF  defaults to .MAC extent for the new file
		       (You can manually type in anything else
		       needed, see examples below.)

	0104h	00  for assemblers other than Microsoft M80
		FF  puts .Z80 and ASEG lines in the new file

	0105h	00  normal Zilog DEFB, DEFS and DEFW codes
		FF  defaults to Intel DB, DS and DW codes

   examples:
   --------

	B>XIZ HELLO <ret>		a)
	B>XIZ HELLO THINK <ret> 	b)
	B>XIZ HELLO.MAC THINK.AZM <ret> c)

   a) Translates HELLO.ASM to HELLO.Z80 (or to HELLO.MAC with 0103h)
   b) Translates HELLO.ASM to THINK.Z80 (or to THINK.MAC with 0103h)
   c) Translates HELLO.MAC to THINK.AZM


FEATURES OF XIZ
===============
	Source code with '!' used for separating several instructions on
the same line is properly converted to individual lines as few non-DRI
assemblers can handle this type of programming.  (Most translators can't
handle this, either, leaving the line only partially translated.)

	Dual colons after global labels are retained.

	Properly reformats the new file with customary fields separated
by tabs.  Inline comments are all moved to a common column position.

	It's FAST.  Using 16k buffers, XIZ runs 2-4 times faster than
most other translators available, such as XLATE or ZCON.  It's somewhat
faster than ITOZ.  It's quiet since there is comparatively little disk
activity.

	It can be used with any 8080, 8085 or Z80 computer.  Most other
translators require a Z80 processor.


USING XZI
=========
	If running an 8080 or 8085, you may have some program that you
want to convert to INTEL source code.  This is not as simple as using an
8080-to-Z80 translator since the Z80 has extra commands not recognized
by the 8080 or 8085 processors.

	XZI shows line numbers of any Z80 code that cannot be changed
to normal 8080 code.  This information is also placed at the end of the
new file generated.  A '#' is included on each of those lines, allowing
an editor to quickly find their location.

	One option is available which can easily be set with DDT or SID:

	0103h	00  defaults to .Z80 extent for the new file
		FF  defaults to .MAC extent for the new file
		       (You can manually type in anything else
		       needed, see examples shown for X80-8 above.)


SIMILAR FEATURES:
================
	Colons are removed after any labels if EQU, MACRO or SET follow.
Colons are added to all other labels, if not already present.  This is a
standard M80 convention which is acceptable to all other assemblers that
are normally used.

	IF, ELSE and ENDIF conditionals are indented one space so they
can be easily seen when studying the source code.

	Progress reports given.  Displays a dot each 100 lines of code
translated.  Ten dots to a group.  Shows total number of lines at end.

	The M80 assembler will not accept asterisks at the beginning of
a full-line comment.  These translators both substitute a semicolon for
such asterisks.  Numerous translators (such as ZCON and prior versions
of these programs) did that after the line had already been capitalized.
Both XIZ and XZI have fixed this problem.

	If a file already exists with the name selected for the output
file, it will notify the operator and ask his further instructions.  A
few other translators just go ahead and erase the other file, which at
times could be disastrous.  (ITOZ even wipes out the original if a 2nd
file is not named.  ZCON does not permit any second file name and also
erases any existing file having the same name it plans to use...)

	Both programs reformat text for normal column locations.  (ZCON
does not.)  This includes putting the inline comments in the same area,
giving an uniform appearance throughout the new file.


COMPARISON:
==========
	A typical 48k 8080 source code program was used for a test.  It
was run on four different translators with the following results:


  Xlator  time			comments

  XIZ	  0:45	  progress reports, no known faults, very fast, free
  ITOZ	  1:11	  commercial, hard to find, barfs on any lower case code
  ZCON	  2:35	  slow, minor problems, cannot specify second file name
  XLATE6  3:31	  good program, progress reports, free, just slow


	A special test was made where the file was run back and forth
through alternating between the two translators several times.	It was
then assembled and the resulting object code compared with that of the
original program.  It was identical.


CREDITS:
=======
	Richard Conn originally disassembled a commercial translator in
the early 1980's and called it XLATE2.	That spawned a number of other
translators, one of which we converted to 8080 source code so it could
be assembled with any normal 8080 assembler and then used on 8080, 8085
or Z80 computers.  At this writing that is up to XLATE6.  It is slow but
does a suitable job otherwise.	Has small buffers, much disk activity.
It does not move comment fields to an uniform area (neither does ZCON).
(That could be easily fixed, but hardly seems worth the bother now that
XIZ is available.)  Frank Zerilli did a very nice job in adding quite
worthy features to XLATE2 and called his version 2.64.	It (like XLATE2)
retained Zilog source code, needed a Z80 assembler and would only run on
computers with a Z80 processor.

	I have rewritten that program for 8080 source code and made many
of the changes already mentioned.  It has been carefully checked for all
8080 to Z80 translations that are shown in normal cross-reference lists.
I gave it a new name, since the changes are so extensive and numerous, I
did not want to destroy the author's original version in case he wanted
to remain associated with that program or preferred the features it has.
I did the same with XZI, starting with the version Frank Zerilli made.


SPECIAL THANKS:
==============
	Joe Wright (an independent commercial programmer) was very help-
ful in testing the program.  He has extensively used macro routines and
other exotic types of pseudo ops, etc.	 He has recently updated VFILER
for ZCPR3 users.  He used that 142k source code as an additional test of
these two programs.  "Before and after" results were the same, when the
comparison was made.

	Other extensive testing has been accomplished and the programs
appear to work as intended.  I hope they will find an useful place among
your other utility routines.  The programs are released for individual
use on a non-commercial basis.
					- Irv Hoff W6FFC
					  Los Altos Hills, CA
					  (415) 948-2166 voice