RECOVER   ver 1.0      05/28/1982
	
    	by Darrell Flenniken
 
 RECOVER is a utility to resurrect programs under Microsoft
 Basic that have been erased from the program buffer by
 NEW or lost by any other means as long as  the program
 buffer remains intact.  Recover is self relocating and may
 placed anywhere in high memory where there is no conflict.
 The desired memory location is specified as parameter when
 recover is loaded.  The size of the relocated module is 
 80 bytes.  If Recover is loaded on top of BASIC, be sure
 to protect memory when loading MBASIC.
 Recover patches into the CP/M bios jump vector table and
 becomes  part of the conin routine and remains active 
 until a  cold boot is performed.

 To use Recover;
		 Exit BASIC via SYSTEM or cold boot. 
		 Load Recover specifying the load address
		      ie, Recover B000
		 Re-load MBASIC and open the same number
		      of files that existed before program
                     loss.
		 When BASIC comes up type CTL-F

 If the program buffer was not destroyed the program will have
 recovered.  LIST the program to assess any possible damage that
 may have occured when the program was lost. 
 Because of the way BASIC initializes the program buffer, the
 first few characters of the first line will be lost, and Recover
 will number the first line as '1'.

 Recover is MBASIC version specific and as of now assembly time
 options are available for MBASIC versions 5.10, 5.20, and 5.21.

 Although not intended for this purpose, Recover will also unprotect
 programs saved with the 'P' option.  Load Recover as usual, load the
 protected program, type NEW, and then type CTL-F and the protected
 program will be unprotected.