KAYPRO 10 GRAPHICS TOGGLE DOCUMENTATION
                     ====== == ======== ====== =============



                                  P R O B L E M
                                  -------------

        The  eight segment graphic characters used with the KayPro 10 are 
        made up of 8 bit characters in the 128 - 255 decimal range,  i.e. 
        the high order bit is set.   (See GRAPHICS.DOC supplied with your 
        machine in the S-BASIC user area for more information).

        When you set a file for READ/ONLY ($R/O), STAT 'sets' the 8th bit 
        of the FIRST character of the filename extension.  This same rule 
        applies  to files set to SYS ($SYS),  STAT 'sets' the 8th bit  of 
        the SECOND character of the filename extension.

        So what you say?   Well have you ever used 'DIR' from MDM7xx only 
        to find some cute little graphic character in place of the  FIRST 
        character of the filename extension on files set to 'R/O' status? 
        Hmmm....  your machine see's that high order bit set so it prints 
        the corresponding eight segment graphic character!  Argh!........

        These  fascinating little graphic characters have appeared on  my 
        machine while using several 'store-bought' programs, besides some 
        public domain software.  Extremely irritating!



                                 S O L U T I O N
                                 ---------------

        GRAF.COM begins by setting up the CONSOLE-OUTPUT routine at EBFDH 
        for an intercept,  pointing to a new routine in high memory.   It 
        then locates a graphics status/bit mask routine to an open  block 
        of  memory beginning at F100H,  then returns control to the  CCP.  
        (F100H to F600H is available in the Kaypro 10).  This status/mask
        routine  checks the graphics toggle byte at F111H,  if set to FFH 
        then the character is passed on normally.  However if the byte at 
        F111H is found set to 00H,  the 8th bit is stripped,  putting  an 
        end to those little graphic characters!

        Run GRAF.COM first, it will load then return to the standard CP/M 
        prompt, A0> (see paragraph below) GRAF.COM will initially set the 
        graphics status byte at F111H to 00H (off),  this may be  altered 
        before  the assembly of GRAF.ASM or with ON/OFF.COM which is also 
        supplied with this library module.

        There are 2 copies of CP/M supplied with your machine, PUTSYS.COM 
        and  NOMENU.COM.  The only difference between them is  NOMENU.COM 
        does not automatically execute the MASMENU program on cold-boot.




                                        1








        We can modify a copy of NOMENU.COM with DDT to automatically  run 
        GRAF.COM on cold-boot.  This way your system can come-alive ready 
        to go in whatever mode you chose before assembly.   Using a copy, 
        NOT the ORIGINAL! execute the following using DDT.COM,

        A0>DDT NOMENU.COM        < -- enter this entire line then return.
        DDT VERS 2.2
        NEXT  PC
        2300  0100
        -S0987                   < -- enter S0987 then return
        0987 00 04               < -- enter 04 then return      (4)
        0988 20 47               < -- enter 47 then return      (G)
        0989 20 52               < -- enter 52 then return      (R)
        098A 20 41               < -- enter 41 then return      (A)
        098B 20 46               < -- enter 46 then return      (F)
        098C 20 .                < -- enter .  then return
        -G0                      < -- enter G0 then return

        warm boot

        A0>SAVE 34 GRAFSYS.COM   < -- enter this entire line then return.

        You  now have a copy of  NOMENU.COM  titled  GRAFSYS.COM which is 
        modified to automatically execute GRAF.COM on a cold-start.  Just 
        type GRAFSYS at the A0> prompt and the new system will be written 
        over  the  old one.   Press RESET on the rear panel and  your  in 
        business.   Now to toggle the GRAPHICS mode use ON/OFF.COM,  poke 
        F111H from Mbasic - Sbasic, or whatever.......



                                    N O T E S
                                    ---------

        GRAF.COM was tested with CP/M version 2.2D for over a month with-
        out any problems.  I'm currently using it with CP/M version  2.2F 
        with no problems noted either.  It's a shame Kaypro did not write 
        something  similar  to this in the BIOS,  although rumor  has  it 
        Kaypro  will begin supplying the source to the 2.2F BIOS in  late 
        1984.  If nothing else we can then re-write the BIOS and use code 
        similar to the present method of setting screen attributes,  i.e. 
        Escape  sequences for triggering inverse video,  blinking  video, 
        underlining, etc.



                                   Tim Montee
                           Vancouver CP/M User's Group









                                        2