OPTION G: General information.

     This  program  is version 1.2 of a screen oriented disk editing  utility, 
loosely  based on the XAMN program that came with many Kaypro  computers,  but 
somewhat more powerful and,  hopefully,  easier to understand.  It is designed 
to  take  advantage  of the cursor movement and video control  of  the  Kaypro 
computers with graphics capability, and is written in Turbo Pascal 2.0.  It is 
also  designed to help the average person find out some things about  the  way 
CP/M operates,  if he is so inclined.  One of the reasons that this file is so 
large  is  that  an  honest  attempt has been made to  explain   some  of  the 
mysteries of the CP/M operating system,  as well as how to use this program in 
a practical sense.  

     In  general,  you will be asked all information necessary to perform  the 
functions listed on the opening menu,  as opposed to other disk utilities that 
expect  you  to memorize commands.   When a numeric value  is  requested,  the 
default  value  (if there is one) will appear on the left enclosed  in  square 
brackets.   This is the value that will be used if <RETURN> is pressed without 
entering a new value.  If a different value is desired, it may be entered from 
the keyboard followed by a <RETURN>,  but it must be within the range shown on 
the  right enclosed in parentheses.   Whenever numeric input is  requested,  a 
hexadecimal number may be entered, which must be preceded by a "$" to indicate 
that the number is hexadecimal,  as in the number $1B.   If a value is entered 
that is not within the acceptable range,  or a syntax error is made, the entry 
will  be  erased  and you will be expected to re-enter it or  press  <RETURN>.  
Some  programs will beep the keyboard to alert the user in such  an  instance, 
but  since  I dislike being audibly corrected by a machine that cannot  think, 
this "feature" has been omitted from the program.  

     While  it  is  possible to interrupt a procedure during the  input  of  a 
numeric value by pressing the <ESC> key, you will also have the opportunity to 
abort  the  process  itself somewhere else along the line.   In  the  case  of 
procedures that write data to the disk, you will always be given the choice to 
terminate  the process before any writing takes place.   Other procedures  are 
interruptible by pressing any key once the procedure has begun.

     String  variables  (text) will also be displayed with the  default  value 
enclosed  in  square brackets on the left.   Again,  if the default  value  is 
desired,  just  press the <RETURN> key without entering anything.   It is also 
possible  with string variables to recall the previous entry (which is usually 
the  default value) for editing by pressing ^R.   You may then add  or  delete 
characters  to the text string using the <BACKSPACE> or <DEL> key.   The <ESC> 
key  may  be  used  at any time to interrupt the input of  string  or  numeric 
variables.

     Single  key inputs,  such as the answer to a yes-or-no question,  do  not 
require  pressing of the <RETURN> key,  and the program does not care  whether 
these single key entries are upper or lower case characters.

     All  processes  that  could potentially require long periods of  time  to 
complete,  and  that  you  may subsequently wish to  stop  once  started,  are 
interruptible by the pressing of any key.  

     If  you  get tired of seeing the opening menu,  you may turn  it  off  by 
pressing  the <ESC> key in place of a selection.   On the other hand,  if  the 
opening menu seems to have unexpectedly disappeared, you may need to press the 
<ESC> key to bring it back.

     There  are  two modes of operation of this  program:  graphics  and  non-
graphics.   To run the program in the graphics mode,  call it like so:  "PROBE 
ON",  and to run it in the non-graphics mode, call it like this:  "PROBE OFF".  
The program is supplied with a default mode that will be used if "ON" or "OFF" 
is  not  typed  when  the program is run,  but the use  of  the  command  line 
parameter allows you to run the program on either machine.   See the technical 
notes for an explanation on how to use this program to change the default  on-
off byte in itself.

     For  those of you with a 6545 CRT controller (which is what is in my  '83 
Kaypro 10),  there is a screen dump utility included that will work within the 
program.   To print the screen, simply press ^@ (control @).  At present, this 
feature works only with the setup described above,  but,  in the future, there 
will  be dumps for the other models as well.   If you have graphics capability 
but  aren't sure whether on not you have this particular controller,  try  the 
screen  dump from the opening menu when operating the program in the  graphics 
mode.  If it works, it works.  If it doesn't...oh, well.

     It  is not possible to damage a disk or file due to inexperience  in  the 
use  of this program unless an improperly modified disk sector is written back 
to the disk.  There are two selections from the main menu where it is possible 
for  this to happen.   The first is Option 0,  which allows you to modify  the 
contents of a disk sector in memory.   However,  after modifying a sector, you 
will  be asked whether or not you wish to write the changes back to  disk:  if 
you  are not sure,  simply choose "N".

     The  other  area where you are likely to get into trouble is  in  copying 
blocks or sectors from one area on the disk to another area when using  Option 
1.   Option  1  is  best avoided until you fully understand what is  going  on 
there.  These  are the ONLY two places in the program where unintentional  and 
irrevocable data loss can occur.

     With these cautions in mind,  you are encouraged to play around with  the 
program  to your heart's content in order to familiarize yourself with it.   A 
suggested  approach  is  to read the help section  for  an  option,  and  then 
experiment  with that option until you understand how it works.   As a further 
safeguard,  practicing  with a "disposable" diskette (a copy of  another  disk 
that will cause no grief if data is lost) is also recommended.

     Good luck.  Rick Ryall, Santa Rosa, CA   1985

OPTION 0: Viewing and/or changing sectors.

     Option  0 allows you to view and change disk sectors.   If this selection 
is  chosen,  you  will  be asked to pick the first track and sector  to  view.  
Default values are enclosed in square brackets on the left,  and the range  of 
acceptable values are enclosed in parentheses on the right.  Pressing <RETURN> 
without entering a new value will cause the default value to be used.

     The first sector will be displayed,  showing the track,  sector,  logical 
block number, data field in hex format on the left, data field in ASCII format 
on the right (there is a one-to-one correspondence between these two  fields), 
and  logical block allocation information (logical blocks are explained in the 
help section for Option 3, disk drive allocation mapping).

     A one line menu will appear at the bottom of the screen:

    (F)orward, (B)ackward, (R)ange, (J)ump, (C)hange, (M)ovement, (ESC)ape

Choosing  (F)  or  (B) will display the next or preceding sector  (or  block), 
respectively.   (R)  sets  the  number  of sectors (or blocks)  that  will  be 
displayed  each time (F) or (B) is pressed,  (J) allows you to jump to  a  new 
sector  (or block) location without exiting to the main menu,  (M) is a toggle 
which  determines  whether to move in sector or block  increments,  and  (ESC) 
exits you back to the main menu.  (C) is explained below.

     Pressing (C) will cause the cursor to be placed on the upper left  corner 
of the data display for the current sector.   You may move the cursor anywhere 
in the data display to change data,  using the arrow keys, with automatic wrap 
around  at the borders (Use of the arrow keys is based on the assumption  that 
the  code sent out when each key is pressed will be the same from one  machine 
to another, which is not always the case.  If you have problems with the arrow 
keys, see note 8 in the Tech Notes help section).

     You may change data bytes in two ways.   First,  you must move the cursor 
over  the  data byte that you wish to change.   If you are in the  hexadecimal 
area on the left side of the screen,  you may enter a hexadecimal number.   As 
you  do  this the corresponding ASCII display will be updated  on  the  right.  
Note that any character code that is not a printing character (like ^C or ESC) 
will appear in the ASCII display as a period,  and that the high bit is masked 
off.   Likewise,  if the cursor is in the ASCII display area on the right side 
of  the  screen,  you  may  enter  a  character  from  the  keyboard  and  the 
corresponding hexadecimal display will be updated on the left.   Note that you 
are  not  allowed  to enter control characters at this  point,  only  printing 
characters.   Pressing  (ESC) indicates that you wish to exit  this  mode,  at 
which  point you will be asked "Do you wish to write these changes to disk  (Y 
or  N)?".   Answering  "Y"  will  write  the displayed  sector  to  the  disk, 
effectively  erasing  the previous data.   Answering "N"  will  redisplay  the 
original  data  and discard the changes.   When in doubt,  answer "N" to  this 
question.

     See  the  technical  notes for the description of what happens  when  you 
change  a  sector  that  is within the logical blocks  assigned  to  the  disk 
directory.

     A final caution when using this option: the program segment used to write 
the sector to disk is the BIOS write routine,  which does not check to see  if 
you  have changed disks between the time the sector was read and the time  the 
revised sector is written.  Therefore, it is possible to read a sector in from 
a disk, remove the disk, insert a different disk and write the modified sector 
onto  the new disk without getting the all-too-familiar "BDOS ERR on A:  R/O".  
Be careful in this regard.

     For those of you unfamiliar with the concept of tracks and sectors,  here 
is a brief explanation.   Each CP/M floppy disk is a thin,  flexible, circular 
device with a magnetic recording material bonded to one (single sided) or both 
(double  sided)  of  its surfaces which can be likened  to  a  flat,  circular 
cassette tape.   When a floppy disk is purchased,  it is like a BLANK circular 
cassette  tape:  there  is no recorded information of any kind  on  it.   Most 
floppy  disks  today  are soft-sectored,  which means that there  is  also  no 
information  of any kind relating to where tracks and sectors  begin,  either.  
That  is  why  a disk must be formatted:  formatting  essentially  puts  "road 
markers" on the disk that define where each track and sector starts and  ends, 
and assigns identifying numbers to each (I think).

     A  track  is a closed circle that shares a common center with  the  disk.  
Information  can be recorded on one of these tracks in basically the same  way 
that information can be recorded on one or the other of the stereo channels on 
a  cassette tape.   There are many of these tracks on a  disk,  starting  with 
track  zero  on the outer edge of the recording area,  and moving  toward  the 
center  in progressively smaller circles.   Remember,  each track is a  closed 
circle (they are not one very long spiral,  like on a stereo record).  So each 
disk is divided up into a number of concentric tracks (double sided disks have 
tracks  on both sides),  which are then each further divided up  into  equally 
sized sectors.   And,  even though the track length gets smaller the closer it 
is to the center of the disk, each track has the same number of sectors in it.  
Sectors are sort of like pie-shaped segments of a track.

     CP/M  defines  a logical sector as being 128 bytes  of  information,  and 
refuses to deal with any other arrangement.   Sometimes, however, it is easier 
to have sectors on a disk (called physical sectors) that are larger than  this 
number,  which  CP/M will allow if the system integrator (in our case  Kaypro) 
will  block  the larger sectors into 128 byte sections when the disk is  read, 
and  deblock  128  byte  sectors  back into  the  larger  physical  size  when 
information  is written to the disk.   This blocking and deblocking is  really 
just  grouping  the  larger physical information blocks  from  the  disk  into 
smaller 128 byte logical blocks (in memory), and vice versa. 

     To summarize,  disks are divided into circular tracks,  which are in turn 
divided  into pie shaped sectors.   When a physical sector is read into memory 
from  the  disk,  it is broken up into a number of 128 byte  blocks.   When  a 
logical sector is viewed using this program,  one of these 128 byte blocks  is 
being displayed. 

OPTION 1: Sector or block copying.

     Option  1  allows a range of sectors (or blocks) to be copied to  another 
area of the logged disk.   This may be useful for reconstructing lost files or 
temporary  storage  when  reformatting a single track  on  the  disk.   During 
copying, the procedure may be interrupted by pressing any key.

     After choosing whether you wish to copy a range of sectors or a range  of 
whole  blocks,  you will be asked for the first track and sector or  block  to 
copy, then how many sectors or blocks to copy (this is the range), and finally 
the first track and sector or block of the desired destination point.  At this 
point you are given a chance to chicken out without writing anything to disk.

     If  you  decide not to chicken out,  you will be asked whether you  would 
like  the  program  to  inform  you  if a  reserved  sector  is  about  to  be 
overwritten.   If  you intend only to copy to sectors that have not  yet  been 
reserved  for  another file,  or you do not feel comfortable with the idea  of 
overwriting reserved sectors, answer "Y" to this question.

     Caution:   this  Option  has  the most potential for creating  havoc  and 
perhaps anguish due to improper or uninformed use and is best avoided entirely 
by  inexperienced users.   There is a bold warning statement in  the  "chicken 
out"  portion  mentioned above,  which highlights the disk drive with  inverse 
video.   There is a reason for this, which is much more important to hard disk 
users: it is quite possible to copy blocks or sectors from one area to another 
ON THE WRONG DISK if you have neglected to log on to the intended drive.  Hard 
disks can be wiped out quite rapidly in this manner, so the moral is pay close 
attention to the "chicken out" message, and especially to the highlighted disk 
drive portion: make sure you are on the right drive.

     Also  note that the copying process will "wrap around" at the last sector 
and begin to copy over track 0 sector 0,  so be careful not to attempt to copy 
a  range of sectors or blocks that is larger than the disk space  between  the 
destination  point  and the end of the disk.   Note also that since  the  last 
block seldom contains a full complement of sectors, it is not usually possible 
to  copy  a  block to the last block on the disk without  beginning  to  "wrap 
around"  to  track 0 sector 0.   Whatever you do,  avoid overwriting the  disk 
directory tracks (unless that is your intent),  or you could have a very large 
mess on your hands.

OPTION 2: File mapping.

     Option 2 allows you to search the disk directory for a filename, and will 
produce a listing of matching entries,  including directory entries that  have 
previously  been  erased but not yet reused by CP/M.   This procedure  may  be 
interrupted  at  any point by pressing a key,  or by pressing <ESC>  when  the 
procedure is paused.

     When a match occurs,  the first item listed on the screen is the filename 
(8 characters) and the extent (3 characters).  If the file name is less than 8 
characters and/or the extent is less than 3 characters, spaces are used to pad 
the  strings  out to the proper length.   The next item displayed is the  user 
number  assigned  to the file (in decimal format),  unless the file  has  been 
erased, in which case the word "Erased" will appear instead.  This is followed 
by  the extent number of the DIRECTORY ENTRY,  the number of 128 byte  records 
(another  term  for  what I call a logical sector) that  the  directory  entry 
references,  and the location of the sector containing the directory entry, in 
track  and  sector format.   The second line will contain the numbers  of  the 
logical  blocks assigned to the file (8 hexadecimal bytes  or  words).   These 
numbers tell where the file data is stored on the disk.  Logical block numbers 
which  are  not  currently allocated (meaning free or not  reserved)  will  be 
highlighted.  Usually, free logical blocks will appear only in files that have 
been  erased,  and  only  then if the blocks have not been  written  over  and 
reserved as part of another file since the erasure.

     When  choosing a filename,  the name may be exact (or unambiguous),  like 
PROBE.COM,  or  ambiguous,  like *.BAK or WS?.COM.   As in many other  utility 
programs, *.* will locate EVERYTHING, meaning all directory entries. 

     Here  are  some  tips on retrieving an erased file.   An erased  file  is 
indicated by the value E5 in the first byte of the directory entry.   You  may 
unerase a file by viewing the sector that contains the entry ( the location of 
which  is  the last item of the first line of each file listing) and  changing 
this  byte  (via  Option  0)  to a  hexadecimal  number  between  00  and  0F, 
corresponding to the user area assigned to the file.  It is not safe, however, 
to  unerase a file that contains logical block numbers that are unhighlighted, 
unless  the block number is zero,  because these blocks have most likely  been 
reassigned  to other files in the time interval since the file was  originally 
erased.   As  a  result,  the  shorter the time  period  between  erasing  and 
unerasing a file, the better the chances of successfully unerasing it.  If you 
erase a file and know that you want to immediately unerase it, DO NOT WRITE OR 
SAVE ANYTHING TO DISK, because all or a portion of the file may be overwritten 
while  it is in the erased condition.   

     When  you  experiment with this option,  you might try this  sequence  of 
operations:   look  at  the  disk  map (Option 3),  erase  a  file  using  the 
previously  described procedure,  and then look at the disk  map  again.   You 
should notice that one or more of the 1's change to a 0.  This illustrates the 
relationship  between  the logical blocks assigned to the file and whether  or 
not  they are reserved,  since erasing a file un-reserves the  logical  blocks 
assigned  to it.   You may also wish to unerase the file and look at the  disk 
map  again  to notice that the 0's are changed back to 1's when this is  done.  
Finally,  you  might like to look at the file map (this option) for  the  same 
file in both the erased and unerased conditions.

     Another  important  note  is  that some large files have  more  than  one 
directory entry associated with them (each of which is called an extent),  and 
in order to unerase these files,  all of the extents must be unerased.  If you 
are unsure about this, ask one of your knowledgeable friends to help you out.

     It  is  also  recommended that files be unerased into a  user  area  that 
contains no other files, to avoid the possibility of having two files with the 
same name appear in the disk directory.   If this should occur,  only the file 
which  appears first physically in the the disk directory will  be  accessible 
since  it  will always be found first in a directory search.   The other  file 
with the same name will appear in the directory but will be inaccessible until 
it is moved to another user area or the first file is erased.

OPTION 3: Mapping of logical blocks.

     Option  3 allows you to produce a map of logical block allocation for the 
currently logged disk drive.   Allocated (reserved) blocks are shown as a "1", 
and  deallocated blocks are shown as a "0".   The decimal block number on  the 
left  corresponds  to the first "1" or "0" displayed in that  row,  while  the 
decimal  number along the top is the offset of the beginning of each group  of 
eight allocation symbols.   To figure out what the block number is for a given 
1 or 0 in the map,  you must first add the offset over the column in which the 
1  or  0 is found to the base number on the extreme left.   This is the  block 
number of the first 1 or 0 in the group of eight that comprise a column.   You 
can probably figure out what to do if the bit you are interested in is not the 
first  in the column,  so we'll leave it at that.   An explanation of  logical 
blocks follows.

     CP/M  divides  a given disk into a fixed quantity of logical blocks  that 
can be reserved (or allocated) for use as data storage areas for  files.   You 
can think of a logical block as a uniformly sized "block" of disk space.  Each 
block is given a unique number; the first block is numbered zero.  The size of 
the  logical block determines the smallest unit of disk space that a file  may 
occupy,  and  all  disk files are even multiples of the  block  size.   Kaypro 
single  density  disks have a block size of 1k,  double density disks  have  a 
block  size  of 2k,  and hard disks have a block size of 4k.   The  first  few 
blocks  are always reserved for the disk directory,  which begins  immediately 
AFTER  the tracks set aside (reserved tracks) for the optional CP/M system  on 
the disk.  Because of this, there is no logical block number associated with a 
disk sector located on one of the reserved tracks.   The number of blocks  set 
aside for the directory depends both on how many directory entries are allowed 
on  the disk,  and how large the block size is,  but the first two blocks  are 
reserved  for  the  disk directory in most cases.   It should  be  noted  that 
logical blocks are also sometimes called "groups" or "allocation groups".

     When a file is erased, CP/M does not actually erase the data in the file.  
Instead,  the hexadecimal byte E5 is written over the user number in the  disk 
directory, which indicates that the directory entry is erased, and the logical 
blocks  that  were  formerly  allocated  (reserved)  for  the  file  are  then 
deallocated  (freed).   Simply stated,  the logical blocks are tagged as being 
unused and are now "up for grabs" to be overwritten on any subsequent saves to 
the disk.   A deallocated block can be reclaimed by entering its block  number 
in  a valid disk directory entry and rebooting the disk,  thereby  making  the 
block  part  of  the file referenced by the  directory  entry.   

OPTION 4: Finding bad sectors.

     This  option allows you to search for bad sectors on the currently logged 
disk.   After the first track and the last track to search have been  entered, 
the  program  reads in each sector and reports any  read  errors  encountered.  
Once the search has begun, the process may be interrupted by pressing any key. 

     The  error  condition  is reported back to the program  by  the  BIOS,  a 
procedure which has its limitations.   The most objectionable is the fact that 
the BIOS does not tag or identify erroneous data in the sector buffer, so that 
the error is reported only on the first physical reading.   

     The  sector buffer is an area of memory set aside to use for reading  and 
writing PHYSICAL sectors to disk,  which may be larger than the CP/M  standard 
128 byte LOGICAL sector.  For example, if the physical sector size on the disk 
is  512 bytes,  as on Kaypro double density disks,  4 logical sectors are read 
into  the  sector  buffer at once.   This is where the  terms  "blocking"  and 
"deblocking" come into play: physical sectors are "blocked" into groups of 128 
byte  logical sectors,  and groups of 128 byte logical sectors are "deblocked" 
into larger (usually) physical sectors.   The physical sector size,  which  is 
always  an  even multiple of 128 bytes to facilitate blocking and  deblocking, 
can be determined by counting the number of times the (F) key must be  pressed 
in Option 1 to cause the disk drive light to come on,  and then multiplying by 
128.   If  the light comes on every time the (F) key is pressed,  the physical 
(on the disk) and logical (in memory) sector size is the same.

     When  a floppy disk or hard disk is physically read by the BIOS,  several 
sectors  are  read  into the sector buffer at once and apparently  stay  there 
until the BIOS is asked to read a logical sector not contained in the  buffer.  
When a read error is reported, there is no way of telling which of the logical 
sectors  in the buffer contain erroneous data.   Furthermore,  if the  logical 
sectors  are  re-read  from  the buffer after having been  accessed  from  the 
physical  disk  once already,  the BIOS will no longer report  that  there  is 
erroneous data, because the disk is not physically accessed.

     What  this means is:   1).  This option will report the first sector in a 
group of logical sectors when a read error is encountered from a physical disk 
read.   2).   You  have  no way of knowing if there is more than  one  logical 
sector in the group that is bad.  3).  Subsequent reads that do not access the 
physical  disk,  such  as when viewing sectors contained in the  buffer  while 
using  Option  1,  will not indicate that there was a read error or  that  the 
buffer contains erroneous data.

     Perhaps someone with some knowledge of floppy disk formatting can rewrite 
the program segment for this option to eliminate these problems.

OPTION 5: Translating track and sector to block number.

     Option  5  calculates the logical block number of the  track  and  sector 
that  you  enter.   You are only allowed to enter a track and sector  that  is 
within  the  logical  block  area of the  disk,  with  the  acceptable  ranges 
appearing on the right as you are asked to input the values.   The  calculated 
values  are  displayed  in  decimal and  hexadecimal  form.   

     Note  that  requesting  the  calculation of a logical  block  alters  the 
default  value  of  the  current  block number by  setting  it  equal  to  the 
calculated value.   

OPTION 6: Translating a block number to a track and sector.

     Option  6 performs a translation from a logical block number to  a  track 
and sector.   It should be noted that the logical block size is always  larger 
than  one  sector,  so the track and sector that are calculated are the  first 
track  and sector in the block.    

     Requesting  the  calculation of a track and sector from  a  block  number 
alters  the  default values of the track and sector variables by setting  them 
equal to the calculated values.   This can be useful when it is desired to set 
the track and sector to the beginning of a block boundary in any of the  other 
options.   For instance, to view a block that was found using the file mapping 
option,  choose this option,  enter the block number, exit this option, choose 
Option  0,  and press the <RETURN> key twice.   The calculated logical  sector 
will then be displayed.

OPTION 7: Logging onto a new disk.

     Choosing  this  option allows you to explore disk drives other  than  the 
default  drive.   It  is  highly  recommended that hard disk  users  do  their 
experimenting  using  the floppy drive (on a floppy disk that has been  backed 
up),  rather  than take a chance on mixing up the large volume of data that  a 
hard disk holds.

OPTION 8: Searching for a text string or byte string.

     Option  8  allows  the  searching of all or parts of a disk  for  a  text 
string,  a byte string, or a combination of both.  After entering the starting 
and  ending tracks to search,  you will be asked to enter the string to  find.  
Pressing the <RETURN> key without entering any new characters will choose  the 
default  string that is displayed,  while pressing ^R will recall the  default 
string so that you may edit it.   ASCII characters with character codes in the 
range  32  to  126 (which are the normal printing characters) may  be  entered 
directly from the keyboard and will appear in the string as normal characters.  
Character  codes outside this range may be entered by pressing the  <TAB>  key 
and  entering  a byte value between 0 and 255.   Normal characters entered  in 
this  manner  will appear as such,  characters in the range 160  to  254  will 
appear  as  inverse video normal characters (if you have  graphics),  and  all 
other codes will appear as hexadecimal numbers.   The <ESC> key may be used to 
abort the procedure at this point.

     After  the search string and search range have been entered,  tracks will 
be  searched  for the desired string.   If the string  is  found,  the  sector 
containing it will be displayed,  and the byte number of the first  occurrence 
in  the  sector  will  be  displayed on line 3  of  the  screen,  followed  by 
up to 12 additional occurrences,  if there are any.  The <RETURN> key may then 
be  pressed  to continue the search,  or,  alternately,  the <ESC> key may  be 
pressed  to interrupt the procedure.   The procedure may also  be  interrupted 
during the active portion of the search by pressing any key.

     This option is useful for finding sectors that have inadvertently  become 
detached  from  files,  such  as  when  part of  a  disk  directory  has  been 
overwritten,  but  some  knowledge of the previous contents are  necessary  in 
order to determine a search string unique to the file in question.

     Since this option does no writing to the disk,  it is very difficult,  if 
not impossible, to accidently harm the disk contents while using it.  

OPTION 9: Exiting to the operating system.

     When  this option is selected,  you are returned to the original  default 
disk  drive and a warm boot is performed,  putting you back in  the  operating 
system (CP/M) on the disk and in the user area from which you started.

OPTION T: Technical notes.
                               TECHNICAL NOTES

1).  The  first  sector  number  of each track is zero  in  the  Kaypro  BIOS.  
Apparently  CP/M will allow the first sector number to be either zero or  one, 
but  there  is no clear way to determine this by asking the operating  system.  
As  a result,  the use of floppy disk formatting compatibility  programs  like 
MFDISK  or UNIFORM or COMPAT to reconfigure the disk drives before using PROBE 
may cause the program to have difficulty finding sector 0 when you ask to view 
it  or copy to it,  because the disk formatting programs may choose  to  begin 
numbering  the sectors with the number 1 instead.   Your choice,  then,  is to 
modify  PROBE  to  take  this into account,  or  not  use  these  programs  in 
conjunction with PROBE.

2).  The  range  of  existing  disk  drives  on  any  given  CP/M  machine  is 
theoretically determinable by polling the BIOS.  In other words, one should be 
able  to find out how many disk drives are on a computer from within a program 
by asking the the operating system.  Specifically, the CP/M manual states that 
when the BIOS SelDisk (select disk) function is called, the address of the DPH 
(disk parameter header) should be returned in the HL register.  In the case of 
a  non-existent drive,  it is the responsibility of the BIOS to return a value 
of  zero  for  the  address,   indicating  that  the  drive  does  not  exist.  
Unfortunately,  the  BIOS  for Kaypro computers is written by Kaypro  and  not 
Digital Research,  and on my CP/M version 2.2F the BIOS is "irresponsible"  in 
this area.   I have a Kaypro 10, which has drives A and B (the hard disk), and 
drive  C (the floppy disk).   However,  the SelDisk function will allow me  to 
select drives D,G,H,K,L,O,  and P without a hint of an error and will actually 
access the floppy disk drive in these instances.   Pretty flaky.   That is why 
the  BDOS  function is used instead of the equivalent BIOS function,  and  the 
constant  LastDisk  is used to limit the choices  to  existing  drives.   This 
constant  may need to be changed and the program recompiled if the number  of 
drives on your computer is fewer or more than the range indicated on Option 7.  
Alternately,  you  may  use  the PROBE program to alter  itself  by  searching 
through  the  file for the constant that limits the disk drive range and  then 
changing it.

3).  This file is expected to be an ASCII text file and will not read properly 
from  within PROBE if it is not.   This is especially a problem when the  file 
has been edited with WordStar,  since WordStar sets the high (or parity)  bits 
of  many  characters during editing.   The command PIP  PROBE.DOC=PROBE.DOC[Z] 
will insure that the high bit of each character is set to zero after this file 
has been edited.   Also,  the procedure that searches for the selected  option 
text  expects  to  find the word OPTION in capitals,  starting  in  column  1, 
followed  by a single space,  followed by the option number or key (uppercase, 
if it applies).  Finally, the last line in this file should be terminated with 
two  carriage  returns,  or it will not print on the screen during use of  the 
help  procedure.   The  program could be altered to allow for  these  possible 
variations, but disk reads and screen output would be significantly slowed.

4).   Since  Kaypro  does  not  use sector skewing and  there  are  no  sector 
translation  tables  in  the BIOS,  there is no provision  to  choose  between 
viewing translated or untranslated sectors in this program.  

5).   The  source code for this program is not what would be  called  "heavily 
commented".   It is assumed that anyone attempting to find out how the program 
works is familiar with Pascal,  and in particular, Turbo Pascal.  Furthermore, 
the  use of vaguely mnemonic variables like DSKNO (for disk number) or r1 (for 
a temporary variable) was avoided wherever it was practical.   The procedures, 
functions and variables have been named, for the most part, using combinations 
of  whole  words  and  titles  which  are  appropriate  for  their   purposes.  
Therefore,  only  those  portions  of  code which  are  somewhat  obscure  are 
commented,  and the rest of the code may be considered to be commented by  the 
intelligent  choice of identifiers.   Since clearness is somewhat  subjective, 
you  may  wish to add comments to portions of the source code  that  you  find 
unclear at first, for the benefit of others.

6).  The complete source program is comprised of the files PROBE.PAS (the main 
file,   which  does  nothing  more  than  call  the  following  three  files), 
PROBE1.PAS,  PROBE2.PAS, and PROBE3.PAS.  To compile this program after it has 
been modified, choose M (for main file) from the Turbo Pascal opening menu and 
enter  PROBE  as the main file name (make sure you are logged onto the  proper 
disk drive first),  then choose O (for compiler option) from the opening menu, 
then  C  (for .COM file) from the options menu,  then Q (for  quit)  from  the 
options  menu,  and  then choose C (for compile) from the opening  menu.   The 
files to be included in the compilation (PROBE1.PAS,  PROBE2.PAS,  PROBE3.PAS) 
will  be  read from the disk automatically.   If the compiler gives  an  error 
message  that indicates that it cannot locate any or all of these  files,  but 
you  know  in fact that they are all together on the disk,  you  are  probably 
logged onto the wrong drive.

7).  The procedure FlushSector is used in the sector editing portion of Option 
0  to  insure  that a physical disk write takes place each time  a  sector  is 
edited.   Otherwise,  it  would  be  possible to edit the changes  in  memory, 
instruct the BIOS to write the sector to disk,  and exit the program with  the 
sector  information  still in the deblocking buffer in memory.   The flush  is 
accomplished rather crudely by reading successive sectors until the buffer  is 
emptied,  and then reading back to the original starting point.  The number of 
successive  sector reads necessary to accomplish this varies with the physical 
sector size and the value chosen was arbitrarily large enough (and then  some) 
to insure that the physical write will always take place.

8).   Option  0 (viewing and changing sectors) uses the arrow keys for  moving 
the cursor around when changing data in the displayed sector.   The arrow keys 
on most Kaypro computers generate the following codes when pressed: Up Arrow = 
^K,  Down  Arrow  = ^J,  Left Arrow = ^H,  Right Arrow = ^L.   In  true  form, 
however,  some machines do not generate these codes,  and while it is possible 
to  alter  the  key  code mapping in the BIOS,  there are  so  many  different 
versions  of  the  BIOS (each of which can be altered by  the  CONFIG  program 
supplied by Kaypro) that this is not really a practical alternative.  In order 
to remedy the problem with your particular machine,  should you have  it,  you 
will  need  either to use the CONFIG program to alter the arrow keys  on  your 
machine so that they generate these codes,  change the source code of PROBE to 
reflect  the codes that your keys generate,  or use the control codes directly 
and forget about using the arrow keys.

9).   Whenever a byte is changed (using Option 0) in a sector that is reserved 
for the disk directory,  the BDOS function 13 (reset all drives) is called  so 
that any changes to the status of a file,  meaning erasure and unerasure,  are 
updated in the allocation map.   For this reason, writing one of these changed 
sectors appears to take longer than normal.

10).  This  is  a somewhat complicated explanation on how you can  change  the 
default  graphics  mode (on or off) of this program  without  recompiling  the 
source  code.   First,  run  the program and log onto the disk  that  contains 
PROBE.   Using  the  file  map  option,  map the program  file  by  typing  in 
"PROBE.COM"  when  prompted and find out which logical blocks are assigned  to 
it.   Write down all the numbers.   Repeat the following  procedure,  starting 
with  the  second block number in the list (I know that it will not be in  the 
first),  until the default byte is found.  Use Option 6 to calculate the first 
track  and  sector in the block.   Remember this.   Then use the  text  search 
function  (Option 8) to locate *.*,  which is the default value for  the  file 
mapping  option.   The  on-off byte you are looking for  immediately  precedes 
this.   You will need to begin the search at the first track and sector in the 
block and end it one sectors-per-block's worth later.  When asked for the text 
string to find,  type in "*.*".  When this string has been found, use Option 0 
to  view the sector that contains it,  and you should see the following string 
of bytes in the hexadecimal field:  03 2A 2E 2A.   The 03 is the length of the 
string  *.*  and  the  next three bytes  are  the  string  itself.   The  byte 
immediately  before the 03 byte is the default graphics mode.   Change it to a 
00 if you want the default to be non-graphics or a 01 if you want graphics.