SUPER-RW          (C) by Eric Gans
			     v. 1.0		last update 12/15/84


	"Super" sounds a bit immodest, but I have done my best to make
this the most practical, versatile and powerful disk/memory utility around.
The latest set of improvements was so extensive that I decided to re-
christen the program.  Since it's now back to version 1.0 that should 
encourage further updates.

	SRW (please rename it something like that; no one wants to type
all those letters) is a general utility program that accesses all
data either on disk or in RAM.  The different options allow the user
to read/write to a track, an allocation block, a file stored on disk,
or the memory, or to search for a string in either hex or ascii.  It has
a hex/ascii string write facility and a Jump command for rapid movement
around the disk/memory.  For greater speed and convenience, prompts
have been reduced to a minimum, so please read the instructions carefully.


                          Instructions

SUPER-RW can be called with or without an operand: srw /command line/ or srw
If invoked alone, the program prompts you for the command line.

COMMAND MODE

	The command line formats are:

(B)lock:  bd:hhh   d = drive | hhh = allocation block number in HEX.
	Example: srw ba:3f (drive A, block 3F)

(T)rack:  td:nnn   d = drive | nnn = track number in DECIMAL.
	Example: srw tc:11 (drive C, track 11)
		
(F)ile:   f[d:]ufn [usr]  (Current drive/user need not be entered.)
	Examples: srw fa:blurk.com 11 | srw fzap.dat 0 | srw fu (Accesses
	a file named "U" in the current drive/user area.)

(M)emory: mhhhh    hhhh = memory address in HEX.  (In order to simplify
	the display, the last digit will be set to 0; thus mffff will
	have the same effect as mfff0.)
	Example: srw ma000
	
(E)xit:   e    Returns to CP/M (no warm boot).

The B, T and F commands give immediate access to the first sector of the
block, track or file selected.


OPERATION MODE

	The options in operation mode are:

D = (D)ump current sector/memory page

N = dump (N)ext sector/memory page

- = back (-)one sector/page

J = (J)ump    This command must be followed by an address:

	Track: Jnn   nn = absolute sector number in DECIMAL.
	            On track 33, J63 will put you in sector # 63 of
		    that track (if it has that many). Sector numbers
		    in tracks/blocks begin with 0.

	Block: Jnn   nn = block-relative sector number in DECIMAL.
		     If the block has 32 sectors then J0 goes to the
		     first and J31 to the last.

	File or Memory:  Jhhhh   hhhh = memory address.  In file mode
                        the address is based on an offset of 100h, but the
		        file is not loaded into memory. Addresses >ffffh
			will wrap around; but files this length are better
			dealt with by examining the allocation blocks in
			the directory.	
  				
S = (S)earch  

	This function permits a search of up to 33 ascii or 11+ hex
	characters.

	Ascii  -  just enter the search string  
	Hex    -  EACH hex byte (1 or 2 digits) must be preceded by ';'	

	This function terminates if the string is found, or if the end
	of the file, block or memory is reached.  To facilitate directory
	searches, in track mode it will search four tracks before giving up.

C = (C)ontinue search

	Searches for the next occurrence of the same string.  This function 
	is only operative IMMEDIATELY following a SUCCESSFUL search.  

W = (W)rite

	First you are prompted for the starting address:

		Memory:   1-byte address (0-FFH)
		
		File:     Either 8 bits or 7 is OK: D7 will be treated
			  the same way as 57.		
	
		Other modes:  7-bit sector address (0-7FH)

	Strings to write follow the same format as for the search function.
	Nothing will be written beyond the current sector/page.

ESC (ascii 27 or 1BH) = (ESC)ape to command mode  (To exit the program,
				                  enter 'E' in command mode.)
		
                              *****

Notes:
	0. This file was written in Z80 code on a Kaypro-10.

	1. I have worked pretty hard on the error-checking, but don't push
your luck!  Remember that entries from the console must be preceded by the
command letter b,t,f or m, and that hex in searches/writes must be preceded
by ';'.  

	2. The Track function will continue on to the next track; if you 
want to step through the disk without returning to command mode, find out
the number of sectors/track and do a J to the last sector followed by an N
to get you to the beginning of the next track.

	3. The Search function distinguishes between upper and lower case.

	4. If you write to disk, the program asks you if you want to
save your work.  It doesn't do this for the memory, since you can always
reset your computer if something goes wrong.

	5. If a disk write has occurred, on exit the disk system will be 
reset. My efforts to limit resetting to individual drives (BDOS function 37)
have led to naught; to avoid "BDOS Error -  R/O" messages you have to
reset the whole thing.

	6. This program makes use of the Disk Parameter Block and should
thus be portable to all reasonable CP/M machines.  It assumes that
(a) the last directory track and (b) sectors/track are one-byte
numbers (<256).  If anyone has a computer for which this is not so, I
would be glad to make the program more general; but are there disks
with 300 sectors per track??  Another assumption in file searches is
that once a formatted sector is encountered (E5 in the area rserved for the
filename, as opposed to the E5 that stands for erasure of a file) one
has reached the end of the directory.  This saves searching four tracks
of a hard disk that has only a few files.  Normally CPM writes to the
directory from the bottom up, so that formatted sectors are virgin territory
and there is nothing beyond them.  If, however, something has gone wrong,
or you have formatted one track in the middle of your directory, the
program won't find all your files.  Either find them via a directory search
(go to the start of your directory in Track mode), or, to fool the program,
put somthing other than E5 in the first byte of the filename (bytes 1,21,41
and 61 of each directory sector).  This can be done using the program
itself.

Further remarks:

	I have toyed with adding a disassembly feature, but there's no
point in competing with SID since the program can't execute the
file in memory.  One thing I have deliberately avoided is full-screen
editing.  It looks pretty, but try changing the last byte (7F) of a
sector when the cursor starts in the upper left-hand corner.  I also
find it inconvenient to overwrite the old bytes during the editing
process.

	Other possibilities: a fully parsed command line as in NULU 
(this might be a bit dangerous for a disk write); an allocation map (see
DMAP in EGUTIL21.LBR); a sector switching/writing facility...

	If you have suggestions for improvement, or find bugs in the 
program, or simply find it useful, I would appreciate hearing from you.

						Eric Gans
						French Department
						UCLA
						Los Angeles, CA 90024