EM211 - 8080A Microprocessor Instruction Set Emulator

        by   Jeffery E. Sheese
             Electronic Engineering Design Technology Program Coordinator
             Detroit Engineering Institute
             2030 West Grand River
             Detroit, Michigan  48226
             (313) 222-7450

        Revision  2.11 - Fixed following bugs:            (JES) 09-06-85
             The backspace key will erase characters on the entry line. 
             The cursor won't backspaced into the command line prompt.
        Revision  2.10 - Rewrote Introduction             (JES) 09-06-85
        Revision  2.00 - Original Release                 (JES) 08-18-82

             The 8080A Instruction Set Emulator is a teaching tool used 
        to demonstrate the operation of the assembly language commands 
        and how they affect the memory and microprocessor register 
        contents.  The emulator was designed to act as a machine language 
        'interpreter', which closely resembles a BASIC interpreter.  This 
        allows the machine language student to operate the computer in a 
        machine language 'direct' mode.  In BASIC, the 'direct' mode is 
        when a person types in a command such as PRINT and watches the 
        results of the command.  The emulator will speed learning and 
        comprehension in a positive and instructive atmosphere.

             When the program is run, a sign-on message is printed on the 
        screen, and immediately following is the prompt:

        Initial status:
        PC    S Z A P C  A  B  C  D  E  H  L  M  SP STACK
        2000  0 0 0 0 0  00 00 00 00 00 00 00 00 0000 0000

        Instruction:   _

             The first line is a description of the type of registers in 
        the microprocessor.  Under each description is the actual content 
        of the register.  The letters S, Z, A, P, and C are the status 
        flags.  They change as the microprocessor status changes.  Their 
        functions and descriptions follow:

        Sign (S)  -    This flag shows if the sign of the result of the 
                       last operation was positive or negative.  The sign 
                       flag will be a 1 if negative, or a 0 if positive.
        Zero (Z)  -    This flag shows if the result of the last 
                       operation was zero.  If the result is zero, the 
                       flag will be 1.  If it was not zero, the flag will 
                       be 0.
        Auxiliary
        Carry (A) -    If the result of the last operation caused a carry 
                       from bit three to bit four of the accumulator, 
                       this flag will be a 1.  Since it is only used for 
                       the DAA instruction, it is generally not tested by 
                       the users program.
        Parity(P) -    This flag shows if the result of the last 
                       operation resulted in an even or odd number of 
                       ones in the resulting byte. It will be a ? if 
                       there is an even number of set bits, or ? if there 
                       is an odd number of ? bits.
        Carry (C) -    This flag shows if the result of the last 
                       operation caused a carry or a borrow from the most 
                       significant bit of the result.  It will be 1 if a 
                       carry or a borrow did occur, or it will be 0 if it 
                       did not occur.


             The rest of the line will show the microprocessor's general 
        purpose registers.  A description of each register follows:

        PC   -    This will show the current address of the program 
                  counter.  Do not let this go below 2000H.  If it does, 
                  you may accidentally alter memory that is essential for 
                  the emulator or the operating system of your computer.

        A    -    This will show the contents of the accumulator after 
                  the last instruction typed.

        B    -    This will show the contents of the B register after the 
                  last instruction typed.

        C    -    This will show the contents of the C register after the 
                  last instruction typed.

        D    -    This will show the contents of the D register after the 
                  last instruction typed.

        E    -    This will show the contents of the E register after the 
                  last instruction typed.

        H    -    This will show the contents of the H register after the 
                  last instruction typed.

        L    -    This will show the contents of the L register after the 
                  last instruction typed.

        M    -    This will show the contents of the memory address 
                  pointed to by the H-L register pair.

        SP   -    This will show the address that is the current  top of 
                  the stack.

        STACK-    This will show the last two bytes that were actually 
                  entered on the stack. This is data, not a memory 
                  address.

             The next thing to do is to actually type in an 8080A 
        mnemonic.  If you have a copy of the 8080A instruction set, you 
        type in the mnemonic the same as if you were entering and 
        executing an assembly language program.  This emulator does not 
        support the use of labels.  All numbers are entered and displayed 
        in hexidecimal format.  After typing in the instruction, press 
        return, and the emulator will display the new status.

        WARNING:
             DO NOT ALTER ANY MEMORY LOCATIONS BELOW 2000 HEX.  THESE 
             MEMORY LOCATIONS ARE ESSENTIAL FOR THE EMULATOR PROGRAM AND 
             THE OPERATING SYSTEM OF YOUR COMPUTER.  THE MNEMONICS AND 
             COMMANDS THAT ARE TYPED IN ARE ACTUALLY STORED AND EXECUTED 
             AT THE ADDRESSES NOTED IN THE PROGRAM COUNTER.













        Authors Note:

             I'm sure many people know the feeling of the initial shock 
        when they write a program and release it into the public domain, 
        and years later find it on an RCP/M board 200 miles away!  This 
        shocked me into the realization that people are actually using 
        this program.  Due to the many bugs present in this program, I 
        definitely feel the need to correct such bugs.  The first step 
        was to seperate the documentation from the actual program source 
        and make quite a few changes in the documentation for clarity.  
        Future revisions will be made to the program to fix the many bugs 
        currently present.

             Future revisions will allow:

        1.   Ascii values to be entered as characters delimited by single 
             quotes (i.e. - mvi a,'G').

        2.   An offset value to be used, plus error checking, to prevent 
             modifying memory required by both the program and the 
             operating system.

             Any other bugs present and found in this program should be 
        reported to the name and address noted at the beginning of this 
        file.  Please feel free to add whatever corrections and features 
        to this program that are necessary, provided these changes are 
        brought to my attention, for everyone to enjoy.  Happy hacking!

                                 - Jeff Sheese -