PRINTER SETUP DOCUMENTATION
    
                             CP/M 2.2 & 3   Ver. 1
    
                            (C) Copyright 1985  PSD
    
    
                        PERIPHERAL SOFTWARE DEVELOPMENT
                             2123 N.E. HALSEY ST.
                              PORTLAND, OR  97232

 
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    

            THE LAST PAGE OF THE DOCUMENTATION WILL EXPLAIN HOW TO
	          BECOME A REGISTERED USER OF THIS SOFTWARE.

    

                        "PRINTSET DOCUMENTATION"                    Page 1

    
    
    





        There are two programs  on  the  distribution  disk;  CONF.COM  and
    PRINTSET.COM.    The PRINTSET.COM is the program that you will be using
    in day-to-day operation.  CONF.COM is  the  program  you  will  use  to
    configure PRINTSET.COM.  CONF actually stands for configure, but due to
    the number of configuration programs already on our systems we  thought
    you  might  appreciate a name that had meaning and yet did not conflict
    with the others.

        This utility is used to preset your printer thus  allowing  you  to
    use programs that have printing capabilities, such as the PIP.COM which
    comes with CP/M or SWEEP.COM from Dave Rand in Canada, that  have  very
    little  or no formatting capabilities.  By presetting your printer, you
    can dump a document and have it printed to allow enough left margin for
    three  ring  binder  holes,  and  in  the case of some of the supported
    printers, allow 1" skip-over perforation.  Some even allow turning  off
    the skip-over function which is very handy when printing program code.

        The very first item to be done is to make a backup of  the  distri-
    bution  disk so that you will have the master available should anything
    happen to your working copy.

        Refer to your computer operating manual if you need  assistance  to
    accomplish this task, or call your dealer.

        Put the master distribution disk away.  DO NOT leave  it  lying  on
    your desk or working area.

        Be sure that both CONF.COM and PRINTSET.COM are in  the  same  user
    area  of  the  same  disk.    Run  CONF.COM  and you will first see the
    copyright notice and BRANDS menu.

        You may pick the letter corresponding to the  manufacturer  of  the
    printer  that  you  own,  or  one of the numerals in the left column to
    define the printer you have (will be discussed further down), or to set
    your  screen  clear and color (or inverse) codes.  If you make an error
    or enter a letter or number not on the screen, the  menu  will  be  re-
    displayed for your choice.

        The printer information (from the menu  or  USER-DEFINED)  and  the
    terminal setup information are independent of each other.  If you don't
    like one or the other when you are finished, you  may  come  back  into
    CONF  and  re-do that one ONLY.  Feel free to experiment with all these
    options.
    

                        "PRINTSET DOCUMENTATION"                    Page 2

    
    
    
     The numeric options include:




        1 = HELP !!!            One screen full of general help  with
                                the configuration.

        2 = ABORT               Get out of the program WITHOUT config-
                                uring PRINTSET.COM.

        3 = SAVE & EXIT         MUST be  used  to save  your  changes
  				whether  you  are  picking  from   the
     				BRANDS and MODELS menus,  setting your
      				screen codes, or defining your printer
        			via the User-Defined option.

        			If  nothing  is entered in  any  area,
	 			choosing  option 3 will do nothing but
                                abort  and put you back to the  system
	  			prompt.

        4 = Terminal Setup      Allows  you to improve the  appearance
 				and   speed  of  the   PRINTSET   menu
  				display.   Follow  the instructions on
                                page 6,  or just leave the defaults if
   				you are in a hurry.

        5 = User-Defined        This option will be necessary if  your
 				printer is NOT listed on the menus, or
				if   you   wish  to  make   your   own
      				CUSTOMIZED menu.

 				WARNING !
  				Read  the  instructions  carefully  to
   				avoid unnecessary work.   The instruc-
    				tions begin on page 4.
      			     



                        "PRINTSET DOCUMENTATION"                    Page 3

    
    /* CHOOSING YOUR PRINTER */

        First we will cover the printer which is made by one of the  listed
    manufacturers.

        This is the easiest part, simply enter  the  letter  next  to  that
    manufacturer  and hit RETURN.  A second or MODEL menu will be displayed
    showing the models currently supported.  Again, enter the  letter  next
    to  the  model  that you have.  At this point, the first or BRANDS menu
    will be re-displayed allowing you to either enter the number correspon-
    ding to one of the items in the left column or if you've made a mistake
    in any of the choices, simply pick the manufacturer again and continue.

        If you choose the SAVE option, the  PRINTSET.COM  program  will  be
    configured from the choices you've made.

    /* SAVING YOUR WORK */
    
        Once you've built a menu and  PRINTSET.COM  has  been  successfully
    configured,  all  that is necessary is for you to COPY the PRINTSET.COM
    file to another name:

                                EXAMPLE:
					PIP EPSON.COM=PRINTSET.COM
				or	PIP PROSET.COM=PRINTSET.COM


        CONF.COM needs the PRINTSET.COM file to be in the same user area of
    the  same  disk.   If you rename PRINTSET.COM to another name, CONF.COM
    will tell you that it 'Cannot  Open  Printset.com'.    Using  the  COPY
    (PIP.COM)  function  of your operating system will make another copy of
    PRINTSET.COM and leave  the  original  intact,  thus  allowing  you  to
    configure  yet  another  printer  or  change the choices you've already
    made.

        DO NOT RENAME "PRINTSET.COM" to another name!!!    Always  use  the
    copy  function  issued  with  your computer or one of the Public Domain
    programs to copy the PRINTSET.COM file to another name.

        When the copy is complete you can  run  CONF.COM  again  and  User-
    Define  your  second  mode  or printer.  Then, as per the example, copy
    PRINTSET.COM to another name.

        The names you choose should reflect (to you) the function  of  that
    file.    Logical  names could be TI-WP.COM or DS-DATA.COM for the Texas
    Instruments Word Processing Mode or  the  Data  South  Data  Processing
    Mode.   Keep in mind that you will have to type the name every time you
    wish to setup the printer so pick a name that is  comfortable  to  you.
    CAUTION:    Stay  away  from  the  one  letter names such as P.COM, the
    reasoning should be obvious.

    

                        "PRINTSET DOCUMENTATION"                    Page 4

    /* USER-DEFINED INSTRUCTIONS */

        In this section of the program it will  be  necessary  to  enter  a
    (possibly)  large number of codes.  Since these must be entered sequen-
    tially, an entry error discovered later  will  necessitate  re-entering
    all  of  the  codes  again.  For this reason, please read the following
    instructions carefully.

        Before attempting to build your first User-Defined menu,  find  the
    three pages within the manual with the 'fill-in-the-blank' lines on the
    right side of the pages.  Make at least three copies of each sheet  and
    store  one  set.    These  will  be necessary if you have more then one
    printer or your printer has multiple modes.  These will help you decide
    what  you would like to see on your menu.  DO NOT attempt to build your
    own without first studying the sheets and filling them out to suit your
    printer.  Use a pencil to fill in the areas you need for your printer.

        Because this program was designed to be a WORKING utility  and  not
    an  elaborate  program  to  spend  hours  involved  with, the menus are
    limited to one screen full, including titles.  That equates to 20 lines
    per  column  including  titles.  As you can see from the three pages of
    material mentioned above, there are  3  columns;  however,  the  middle
    column  has many more then 20 options.  Therefore it will be necessary,
    if your printer has  above  average  capabilities  or  is  of  the  15"
    carriage  variety  and  can  have the right margin set, for you to make
    some choices as to what you want within the column's boundaries.

        You will be asked a number of questions dealing  with  the  control
    codes  for  your  printer.   These codes will need to be entered in HEX
    format.  Most printer manuals show the control codes  in  ASCII  format
    but have an example in hex.

        If you need it or  would  rather  use  it,  we've  included  a  HEX
    conversion chart at the end of this documentation.

                                 EXAMPLE:       ESC Y
					     chr$(27), chr$(89)
					     (1b,59)

        Your manual will at the very least show a sequence like  the  first
    line in the example above.  From that point, manuals differ greatly and
    you may have to refer to a page (normally toward the back)  which  will
    have  a  chart  showing the equivalent of the second and third lines of
    the example.

        To begin USER-DEFINED select number 5 from the  main  menu.    Have
    your prepared fill-in sheets ready.

        You will be  offered  a  number  of  options  under  various  title
    headings.   They will be presented in the same order as the ones on the
    three pages of fill-ins.
    

                        "PRINTSET DOCUMENTATION"                    Page 5




        If you make a typing error while entering the data into one of  the
    lines  you  may  use  the  backspace key to edit the line.  If you have
    entered a RETURN and then discover that  an  error  was  entered  on  a
    previous  line you will NOT be able to go back to that line and fix it.
    The only solution is to enter a slash ( / ) which will  return  you  to
    the  BRANDS menu.  Then you will have to enter number 5 again and START
    OVER.

        The resulting menu may not be as elaborate  as  some  of  the  ones
    we've  developed.    For  example,  if  your  printer has multiple mode
    capability, such as Data Processing, Word Processing,  and  IBM  Compa-
    tible, you will need to build a separate menu for each mode.

        Building separate menus whether it be  for  different  printers  or
    printers  with  multiple  modes  will not be hard after you've done the
    first one.

    

                        "PRINTSET DOCUMENTATION"                    Page 6

    /* TERMINAL SETUP */

        Whether you pick from the BRANDS and  MODELS  menus  or  choose  to
    define  your  own, you have the option of entering the clear screen and
    colors desired (or inverse on and inverse off for monochrome) for  your
    terminal or computer.  This function is accessed by entering the number
    next to SET SCREEN CODES located in the left column.  Once entered, you
    will  be  faced  with the same situation as the User-Defined printer in
    that all answers to the prompts MUST BE answered in HEX.

        Your computer or terminal manual will have the codes listed  within
    it  to allow at least the clear screen, and probably the inverse on and
    off.

        Refer to the back of  this  documentation  for  the  ASCII  to  HEX
    conversions and enter them according to the prompt.

        Read the HELP screens CAREFULLY!   You  will  see  that  the  input
    request  line  states  that  there  are  10  and  20 HEX codes of space
    available depending on  whether  you  are  inputting  clear  screen  or
    inverse  video.  One HEX code is actually two characters.  For example,
    an ESC or Escape character is 1B in HEX, and 27 in decimal.  When  your
    manual  states that the code for INVERSE ON is 'ESC j', this means that
    you would need to enter '1B,6A' into the input request line for Inverse
    On,  separating  the  characters  with a comma preferably and NO spaces
    after the comma.

        The screen options may be changed by running CONF again and picking
    the  number next to TERMINAL SETUP and again answering the questions in
    HEX.  If you're satisfied with the printer menu as you had designed it,
    you will find it un-necessary to re-enter the printer.
    

                        "PRINTSET DOCUMENTATION"                    Page 7

    /* RUNNING PRINTSET.COM */

        To run your configured printer setup program,  just  type  PRINTSET
    (or  the  name  of the copy -- EPSON, for example).  This will bring up
    the menu for the printer you have selected or USER- DEFINED.   Now  you
    may  enter  as many choices as you please.  Functions will be performed
    in the same order that you type them.  For example, if  you  are  using
    the EPSON FX-80, typing

                                 8AP [RETURN]

    (the letters may be upper or lower case),  will:

        1. do a software reset (restore printer to power-on defaults)

        2. set the elite font

        3. set the left margin to a width of 15 characters


    If you don't wish to see the menu, then simply type

                             PRINTSET 8AP [RETURN]

    to accomplish the same thing faster.

        You may find during use that, contingent to  the  printer  you  are
    using,  the left margin will vary according to the print size selected.
    Not all printers have this capability, some call 1" left  margin  a  1"
    left margin, while others adjust according to the pitch selected.

        If yours has this capablity then you will surely find that  instead
    of having just the margins available from the menu, you will be able to
    double that by turning on the printer, running PRINTSET.COM or whatever
    you have renamed it, and selecting the left margin before selecting the
    PRINT SIZE.

    The logic is this:
    
               If you select a left margin of 10 and are  in  the  power-up
    state on the printer (either just turned on or reset) the default print
    size will probably be Pica or 10 CPI.  Therefore, the left margin  will
    be  adjusted  according  to Pica size.  Then changing to Condensed size
    will give you the same physical left  margin  as  the  Pica,  about  16
    characters  in Condensed, or 1".  If on the other hand you request from
    the menu a change to another PRINT SIZE before requesting a left margin
    setting, the left margin will be adjusted according to that PRINT SIZE.
    Thus Condensed with a 10 left margin would give a left margin of 5/8".
    

                            "PRINTSET DOCUMENTATION"                Page 8
    
    

        Another fun item to play with is the capabilities of some  printers
    to allow the combining of multiple PRINT TYPES.  A good example of this
    would be combining Condensed, SuperScript, and Italics.  If you thought
    it  was  nice  to be able to print 132 columns on an 8" sheet of paper,
    wait till you see this.







                        ******************************
                        *   User-Supported Software  *
                        ******************************

        If you are using  this  program  and  finding  it  of  value,  your
    contribution ($14.95 suggested) will be appreciated.  Please be sure to
    include your name and address ( & phone number if you like ) along with
    your contribution.
    
        You will become a REGISTERED USER by sending a contribution to the
    address below.
    
        We will be happy  to  give  any  assistance  to  registered  users.
    Registered  Users  will  be the first notified of any future updates or
    revisions, as well as any New Software developed.


    
    

                                 **** PSD ****
                               2123 N.E. Halsey
                              Portland, OR  97232
                                (503) 249-0627
    
        You are encouraged to copy and share this program with other users,
    on  the  conditions that the programs and documentation are not distri-
    buted in modified form, that no fee or consideration  is  charged,  and
    that this notice is not bypassed or removed.



        *** 1st Column ***                 [ ENTER YOUR CODES HERE ]

    .PRINT SIZE.=
             Normal Pica Print ------ ____,____,____,____,____,____
             Elite Print ------------ ____,____,____,____,____,____
             Condensed Print -------- ____,____,____,____,____,____
             Condensed OFF ---------- ____,____,____,____,____,____
             Proportional Print ----- ____,____,____,____,____,____
             Proportional Spacing --- ____,____,____,____,____,____
             SuperScript ------------ ____,____,____,____,____,____
             SuperScript OFF -------- ____,____,____,____,____,____

    .PRINT TYPE.=
             Italics Print ---------- ____,____,____,____,____,____
             Italics Print OFF ------ ____,____,____,____,____,____
             Emphasized Print ------- ____,____,____,____,____,____
             Emphasized OFF --------- ____,____,____,____,____,____
             Shadow Print ----------- ____,____,____,____,____,____
             Double Width ----------- ____,____,____,____,____,____
             Double Width OFF ------- ____,____,____,____,____,____
             Correspond Quality ----- ____,____,____,____,____,____
             Correspond Qual OFF ---- ____,____,____,____,____,____


    *** Middle Column ***

    .LINE SPACING.=
             3 Lines Per Inch ------- ____,____,____,____,____,____
             4 LPI ------------------ ____,____,____,____,____,____
             6 LPI ------------------ ____,____,____,____,____,____
             8 LPI ------------------ ____,____,____,____,____,____
             9 LPI ------------------ ____,____,____,____,____,____
             12 LPI ----------------- ____,____,____,____,____,____

    .LEFT MARGIN.=
             3 Characters ----------- ____,____,____,____,____,____
             5 ---------------------- ____,____,____,____,____,____
             7 ---------------------- ____,____,____,____,____,____
             10 --------------------- ____,____,____,____,____,____
             12 --------------------- ____,____,____,____,____,____
             15 --------------------- ____,____,____,____,____,____



 

    *** Middle Column Cont. ***        [ ENTER YOUR CODES HERE ]

    .RIGHT MARGIN.=
             5 Characters ----------- ____,____,____,____,____,____
             7 ---------------------- ____,____,____,____,____,____
             10 --------------------- ____,____,____,____,____,____
             12 --------------------- ____,____,____,____,____,____
             15 --------------------- ____,____,____,____,____,____

    .80 COL RIGHT MARGIN.=
             5 Characters ----------- ____,____,____,____,____,____
             7 ---------------------- ____,____,____,____,____,____
             10 --------------------- ____,____,____,____,____,____
             12 --------------------- ____,____,____,____,____,____
             15 --------------------- ____,____,____,____,____,____

    .132 COL RIGHT MARGIN.=
             5 Characters ----------- ____,____,____,____,____,____
             7 ---------------------- ____,____,____,____,____,____
             10 --------------------- ____,____,____,____,____,____
             12 --------------------- ____,____,____,____,____,____
             15 --------------------- ____,____,____,____,____,____


    (NOTES):











    cont. next page



    *** Right Column ***               [ ENTER YOUR CODES HERE ]

    .PRINT MODE.=
             Quiet Mode ------------- ____,____,____,____,____,____
             Draft Mode ------------- ____,____,____,____,____,____
             Near Letter Quality ---- ____,____,____,____,____,____
             Line ------------------- ____,____,____,____,____,____
             Serial ----------------- ____,____,____,____,____,____
             Logic Mode ------------- ____,____,____,____,____,____
             Incremental Mode ------- ____,____,____,____,____,____
             Word Processing Mode --- ____,____,____,____,____,____
             Data Processing Mode --- ____,____,____,____,____,____
             IBM Mode --------------- ____,____,____,____,____,____

    .PRINT DIRECTION.=
             Uni-Directional -------- ____,____,____,____,____,____
             Bi-Directional --------- ____,____,____,____,____,____

    .Misc Print Codes.=
             Double Strike ---------- ____,____,____,____,____,____
             Double Strike OFF ------ ____,____,____,____,____,____
             Underline Print -------- ____,____,____,____,____,____
             Underline OFF ---------- ____,____,____,____,____,____
             Right Margin ON -------- ____,____,____,____,____,____
             Right Margin OFF ------- ____,____,____,____,____,____
             Skip Over Perf --------- ____,____,____,____,____,____
             Skip Perf OFF ---------- ____,____,____,____,____,____
             Cancel Buffer ---------- ____,____,____,____,____,____
             Auto Justify ----------- ____,____,____,____,____,____
             Form Feed -------------- ____,____,____,____,____,____
             Software Reset --------- ____,____,____,____,____,____

    (notes):


	    Decimal - Hexadecimal - ASCII    Conversion Chart


 Decimal    HEX  ASCII       Decimal    HEX  ASCII       Decimal    HEX  ASCII
or CHR$(n)                  or CHR$(n)                  or CHR$(n)


    0        00   NUL          43        2B    +           86        56    V
    1        01   SOH          44        2C    ,           87        57    W
    2        02   STX          45        2D    -           88        58    X
    3        03   ETX          46        2E    .           89        59    Y
    4        04   EOT          47        2F    /           90        5A    Z
    5        05   ENQ          48        30    0           91        5B    [
    6        06   ACK          49        31    1           92        5C    \
    7        07   BEL          50        32    2           93        5D    ]
    8        08   BS           51        33    3           94        5E    ^
    9        09   HT           52        34    4           95        5F    _
   10        0A   LF           53        35    5           96        60    `
   11        0B   VT           54        36    6           97        61    a
   12        0C   FF           55        37    7           98        62    b
   13        0D   CR           56        38    8           99        63    c
   14        0E   SO           57        39    9          100        64    d
   15        0F   SI           58        3A    :          101        65    e
   16        10   DLE          59        3B    ;          102        66    f
   17        11   DC1          60        3C    <          103        67    g
   18        12   DC2          61        3D    =          104        68    h
   19        13   DC3          62        3E    >          105        69    i
   20        14   DC4          63        3F    ?          106        6A    j
   21        15   NAK          64        40    @          107        6B    k
   22        16   SYN          65        41    A          108        6C    l
   23        17   ETB          66        42    B          109        6D    m
   24        18   CAN          67        43    C          110        6E    n
   25        19   EM           68        44    D          111        6F    o
   26        1A   SUB          69        45    E          112        70    p
   27        1B   ESC          70        46    F          113        71    q
   28        1C   FS           71        47    G          114        72    r
   29        1D   GS           72        48    H          115        73    s
   30        1E   RS           73        49    I          116        74    t
   31        1F   US           74        4A    J          117        75    u
   32        20   SP           75        4B    K          118        76    v
   33        21   !            76        4C    L          119        77    w
   34        22   "            77        4D    M          120        78    x
   35        23   #            78        4E    N          121        79    y
   36        24   $            79        4F    O          122        7A    z
   37        25   %            80        50    P          123        7B    {
   38        26   &            81        51    Q          124        7C    |
   39        27   '            82        52    R          125        7D    }
   40        28   (            83        53    S          126        7E    ~
   41        29   )            84        54    T          127        7F    DEL
   42        2A   *            85        55    U