SAP-FIX.DOC as of 5/22/80
		 by Keith Petersen, W8SDZ

   If you are using CP/M-2 and have SAP.COM on your system,
you probably have noticed that the directory sorting gets
confused by the file attributes used in CP/M-2.  This can
be easily fixed by modifying your COMP1 routine to read as
seen below.  This fix applies to all versions of SAP, whether
you have single or double density.

;
COMP1:	MOV	A,M		;GET NEXT BYTE
	ANI	7FH		;REMOVE ATTRIBUTES
	MOV	B,A		;SAVE IN B
	LDAX	D
	ANI	7FH		;REMOVE ATTRIBUTES
	CMP	B		;COMPARE CHARACTER
	RNZ			;RETURN IF NOT EQUAL
	INX	D
	INX	H
	DCR	C		;LOOP THRU FIRST 13 BYTES
	JNZ	COMP1
	XRA	A		;CLEAR FLAGS AND EXIT
	RET
;

END OF SAP-FIX.DOC