VOIC@.DOC

       DOCUMENTATION FOR VOIC@ LANGUAGE SYSTEM FOR SPEECH SYNTHESIS

	   WRITTEN & RELEASED IN PUBLIC DOMAIN BY AL JEWER, 
	    SHAWN EVERSON,AND WILLIAM WHITFORD, 10/21/81



THIS DOC FILE EXPLAINS THE USE OF THE VOIC@ SOFTWARE
PACKAGE FOR USE WITH THE SWEET TALKER SPEECH BOARD AND A
Z80 CPU WITH PARALLEL PORT INTERFACE.
ANY OTHER BOARD USING THE SC-01 VOICE SYSTHESIS CHIP FROM
VOTRAX SHOULD BE ABLE TO BE SUPPORTED WITH A MINIMUM OF
PROGRAM MODIFICATIONS.

THIS CODE IS WRITTEN FOR USE WITH AN 8255 PARALLEL PORT
INTERFACE CHIP. THE ONLY HARDWARE DEPENDANT ROUTINE IS
IN VOIC@.LIB, WHICH PROVIDES SETUP FOR THE 8255 AT BASE 
ADDRESS 24H AND READS & WRITES TO ITS PORTS. ANY OTHER
PARALLEL PORT INTERFACE COULD BE USED BY RE-DEFINING
THE PORT ADDRESSES FOR YOUR PARTICULAR HARDWARE.

THE PROGRAMS INCLUDED IN THIS PACKAGE ARE:

		VMAC.ASM     -> THE MAC ASSEMBLER OVERLAY
		VRMAC.ASM    -> THE RMAC ASSEMBLER OVERLAY
		VOIC@.LIB    -> THE DRIVER FOR CP/M, PHONEME
				DEFINITIONS AND DICTONARY.
		VOIC@EQU.LIB -> SAME AS ABOVE MINUS DICTONARY
		TALK@.LIB    -> STARTING PLACE FOR WRITING NEW 
				VOICE PROGRAMS
		YESMASTR.VOC -> EXAMPLE PROGRAM WHICH HAS A 
				GOOD ATTITUDE.
		VOIC@.CRC    -> CRC'S OF ALL PROGRAMS
		VOIC@.DOC    -> THIS FILE


TO MAKE IT TALK:

1) CREATE A FILE OF TYPE .VOC (STARTING WITH TALK@.LIB) WHICH
	CONTAINS THE WORDS YOU WANT TO SAY, ONE PER LINE.
	UNIQUE WORDS CAN BE DEFINED AS PHONEMES. (SEE YESMASTR.VOC
	FOR DETAILS & EXAMPLE OF HOW TO DO THIS).

2) ASSEMBLE ABOVE FILE USING VMAC OR VRMAC TO CREATE A .HEX OR .REL
	FILE FOR USE BY THE LOADER (OR LINKER).

3) FOR VMAC: USE LOAD AS YOU WOULD WITH ANY .HEX FILE, TO CREATE A
	.COM FILE WHICH WILL TALK TO YOU.
   FOR VRMAC: USE LINK TO CREATE A .COM FILE, OR DECLARE A MODULE NAME
	AND LINK TO YOUR OTHER PROGRAMS!!!!

4) LISTEN TO IT!!!!



TO CREATE VMAC OR VRMAC:

READ VMAC OR VRMAC.ASM TEXT, AND FOLLOW DIRECTIONS THERE. YOU CANNOT
ASSEMBLE THESE FILES USING MAC OR RMAC, SINCE SOME OF THE WORDS 
DEFINED IN VOIC@.LIB ARE NORMALLY RESERVED WORDS IN MAC. WATCH OUT!
THE PSEUDO-OPS IN MAC HAVE BEEN CHANGED! CONSULT VMAC.ASM & VRMAC.ASM
FOR ALL PSEUDO-OP CHANGES. THANK YOU.

ANY QUESTIONS OR COMMENTS, FEEL FREE TO CALL US AT:

 (414) 563 8774 

IF YOU GET A TONE, WE'RE NOT HERE. IF SOMEONE ANSWERS, ASK FOR
AL JEWER, SHAWN EVERSON OR WILLIAM WHITFORD. WE ARE THE VOICE 
SYNTHESIS GROUP HERE, AND WILL BE GLAD TO ANSWER ANY HOBBYIST 
QUESTIONS REGARDING OUR SPEECH SYNTHESIS SOFTWARE.
BY THE WAY, THIS IS PUBLIC DOMAIN SOFTWARE, AND IS NOT TO BE 
SOLD OR DUPLICATED ENDLESSLY FOR PROFIT. WE WROTE THIS FOR THE 
HOBBYISTS, SO COPY IT ALL YOU WANT, JUST DON'T SELL IT.

YOU CAN WRITE US AT:

		VOICE SYNTHESIS GROUP
		LAB 1
		214 SOUTH MAIN STREET
		FORT ATKINSON, WISCONSIN 53538